## Slide 1: SPICE modeling for Langmuir probe simulation and estimating spacecraft charging
  Aroh Barjatya
  Space and Atmospheric Instrumentation Laboratory
  Embry-Riddle Aeronautical University
  sail.erau.edu

## Slide 2: Langmuir Probe Basic Theory
Typical Op-Amp based Langmuir probe circuit and an I-V curve

## Slide 3: Langmuir Probe Basic Theory …Contd.
Notes: Plasma...Energy equivalent==>Electrons fast... thus if only ion and electron currents then the spacecraft charges negative.
PE important at GS high altitudes...
Also talk about sheath at this point… how sheath shield the plasma from any fields…

## Slide 4: SPICE
SPICE - Simulation Program with Integrated Circuit Emphasis
An industry standard simulation program used by electrical engineers for simulating networks of linear and non-linear circuit elements. [Keown, 2001]
Uses numerical methods to solve non-linear equations
70+ years of heritage
Multiple commercial options: Cadence PSPICE, Analog Device’s LT Spice, ngSpice, gnuCAP, and many more. All use similar programming syntax.

## Slide 5: Sample SPICE Program
The SPICE programming file extension is *.cir
All comments begin with a semicolon ( ; )
“.PARAM” sets global variables/constants
R, C, L, V, etc have their regular meaning
You specify Rxx, Cxx, Lxx, Vxx for specific devices
The .cir file should always end with “.END”
Node 0 is always the circuit Ground and each device needs to be connected between two nodes… just like on a breadboard. If not specified its assumed to be node 0, i.e. GND. You cannot have floating nodes.
Typically nodes are numbered and specified immediately after the device type and the third number is the value assigned to the device
  R 3 2 100 or R 3 2 1meg or C 3 2 5u or L 3 2 1m
X is a special device used for “.subckt” i.e. a function

## Slide 6: SPICE scaling factors
You can specify the same value in many different ways although be careful with CASE as different spice compilers handle them differently.

## Slide 7: Types of sources

## Slide 8: Types of Control Statements

## Slide 9: Introducing Sub-Circuits in SPICE
Create a Voltage-Dependent-Current-Source, specified with element “G”
Use Langmuir Probe Current Collection Equations
Spacecraft Conducting Surface
Vf
Vp
Plasma
Gi
Ge
=
subckt

## Slide 10: Variation of plasma parameters

## Slide 11: Doing multiple subcircuits with different geometries

## Slide 12: Simulating Various Geometries of Langmuir Probes
Vlp
+
-
Cyl
Probe
Surface
Vp
Pla
Probe
Sph
Probe
1
3
0

## Slide 13: Understanding Floating Potential

## Slide 14: Simulating Area Ratio Effects
Vlp
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e+
E+
E+
E+
E+
E+
E+
E+
E+
E+
E+
E+
+
-
Probe
Surface
Ip
Ir

## Slide 15: Simulating Area Ratio Effects… contd
S/C charges to -0.25 V
i.e. more positive than otherwise !
LP is applied voltage w.r.t the S/C chassis ground.
As LP sweeps positive and collects more electron current, the S/C chassis charges more negative… LP never makes it past Vp
Applied Voltage w.r.t. Vs/c
Voltage w.r.t. Vp

## Slide 16: Simulating Area Ratio Effects… contd
S/C now charges to nominal -0.3 V
LP sweeps still charges the spacecraft surface, but this time LP does make it past Vp.
Applied Voltage w.r.t. Vs/c
Voltage w.r.t. Vp

## Slide 17: Simulating Area Ratio Effects… contd
Note the parametric sweep above
S/C charges to -0.3 V
As the S/C to probe ratio increases beyond 103 the charging effect becomes negligible, and approaches zero at 104.
This was also analytically shown by Szuszczewicz [1972].
Voltage w.r.t. Vp

## Slide 18: Case Study – EQUIS II Rocket
Rocket Launched from Kwajalein, Aug 2004
Ratio of payload surface area to that of combined SLP probe + guard surface area was about ~120

## Slide 19: Spacecraft Charging
IE = Electron Current
II = Ion Current
IRAM=Ram Current
IPH=Photoelectron
ISE=Secondary Electron
IBSE=Back Scatter
IB=Beam/Ion thruster
Vp = Floating Potential / Charging
[IE (Vp) + IB(Vp)] - [ II (Vp) + IRAM (Vp) + IPH(Vp) +ISE(Vp) + IBSE(Vp)] = 0
[Outgoing current - Incoming current] @ floating potential = 0

## Slide 20: Case Study – EQUIS II Rocket
SPICE Model

## Slide 21: Case Study – EQUIS II Rocket
  Model Results: Sweep ‘warping’ due to small area ratio.

## Slide 22: Case Study – EQUIS II Rocket
  Observed Data
  Affected by SLP sweeps as well as PSP sweeps.

## Slide 23: Case Study – Sudden Atom Layer Rocket
Flight: 19th Feb 1998, Puerto Rico 2009 LT
Investigation of sporadic sodium layers
Dust Detector
Floating Potential Probes
Swept Impedance Probe
DC Langmuir Probe (DCP)

## Slide 24: Case Study – Sudden Atom Layer Rocket
Charged Dust Layer

## Slide 25: Case Study – Sudden Atom Layer Rocket

## Slide 26: Case Study – Sudden Atom Layer Rocket

## Slide 27: Case Study – Sudden Atom Layer Rocket
Circuit model in SPICE
Using Cylindrical OML equations
With correct probe to skin area ratios
S/C Charging Potential = -1.3 Volts

## Slide 28: Case Study – Sudden Atom Layer Rocket
Triboelectric Charging:
When two metal surfaces come in contact with each other and then separate, the metal surface with lower work function gets charged positive and the other surface gets charged negative
Work function: Aluminium: 4.2eV Sodium: 2.36eV
Dust current: modeled as RAM current
 Dust source of electron current

## Slide 29: Case Study – Sudden Atom Layer Rocket
Observed Dataset
Triboelectric Charging
Simulation Results

## Slide 30: Understanding Floating Potential
First… Lets look at detailed Floating Potential of Probe and Surface when area ratio is 10,000
Notice that V(1) (i.e. surface) charges by 0.8mV when ratio is 10K. Negligible, but not zero.
When ratio is 20K. Charging is in uV and not discernible.

## Slide 31: Understanding Floating Potential… contd
Second… Lets look at detailed current and potentials of surface and Langmuir probe
So essentially, the “Zero current” is at 0 applied potential. Because Langmuir probe is now at same potential as the surface which is floating!

## Slide 32: Understanding Floating Potential… contd
Third… Lets look at detailed current and potentials when extraneous charging is there
Langmuir probe reaches *its* Floating Potential at same -0.297V w.r.t. plasma, but the Payload is charged a bit more negative (-1.13V to be exact) in order to balance the current coming from Xerr extraneously biased surface.
Thus, now the Langmuir probe has to bias +1.13 V to reach its Zero current value which makes it reach its floating potential of -.297 w.r.t. plasma.
This implies that the applied Vslp that results in Islp=0 is the additional charging of the payload and *not* the true floating potential of the payload.

## Slide 33: Understanding Floating Potential… contd
Fourth… How bad does it get with contamination and hysteresis… Lets look at Dynamo2
There is no significant charging!
Note that Vslp = V(3)-V(1).
So the current zero crossing is
at essentially zero applied Vslp voltage.

## Slide 34: Understanding Floating Potential… contd
Fourth (contd)… Lets add charging
Now charging to -0.44V as seen by
SLP, but no hysteresis and the real
charging relative to plasma is -.75V

## Slide 35: Understanding Floating Potential… contd
Fourth (contd)… Lets add reasonable RC on probe
No meaningful hysteresis.
No matter what reasonable RC
values we give.

## Slide 36: Understanding Floating Potential… contd
Fourth (contd)… Lets add RC on the payload surface
V(3)-V(9) =
UpSweep = +.78
DownSweep = +1.177
True surface potential is V(1) which is about -.69V w.r.t. plasma during upsweep and -.62 V during downsweep.

## Slide 37: Summary
Several SPICE programs are commercially available either as freeware or for minimal costs.
The numerical solvers available within SPICE can be used to rapidly and simultaneously calculate spacecraft floating potential, as well as instrument response, including all the transient capacitive effects… correct within the order of magnitude.
Such modelling is relatively easy to do and should be done for every mission where Langmuir probes are part of the mission.